## Slide 1
Copyright 2024 California Institute of Technology.
U.S. Government sponsorship acknowledged.
Douglas S. Abraham, Shantanu Malhotra, Leila Meshkat, David D. Morabito, James A. O’Dea, Emily R. Pascua, Marc Sanchez-Net, Dong K. Shin, Luke C. Stewart, and Zaid J. Towfic
Jet Propulsion Laboratory, California Institute of Technology
Interplanetary Small Satellite Conference
University of Arizona, Tucson, AZ
April 30, 2024 – May 2, 2024
Deep Space Network
Multiple Uplinks Per Antenna (MUPA): Where Are We Now?

## Slide 2: What Is MUPA? (1/2)
Traditional Multiple Spacecraft Per Antenna (MSPA)
Uplink During MSPA
Commanding and 2-way Doppler & ranging must occur 1 spacecraft at a time with reconfiguration time in between.
Downlink
During MSPA
Frequency Division Multiplexing

## Slide 3: What Is MUPA? (2/2)
Multiple Uplinks Per Antenna (MUPA)
Command Link Transmission Units (CLTUs) intended for each in-beam spacecraft are time-multiplexed onto a single frequency uplink that all the spacecraft receive and process.
Each spacecraft discards the transfer frames having an improper SCID in the header.
Allows near-simultaneous commanding and simultaneous 2-way Doppler & ranging.
Time Division Multiplexing

## Slide 4: In What Situations Would MUPA Work? Anywhere MSPA Does
Concentrations of lunar surface assets such as those planned for near the Moon’s south pole would be in-beam, even at K-band.
Future secondary payload deployments – Artemis, ESPA rings, Blue Ring, etc.
Most everything at Mars or Venus is within the half-power beam-width of a 34m antenna at S- and X-band. Ka-band has some orbital altitude dependence when the planets are closer to Earth.
If designed to be in-beam, constellations of spacecraft or flotillas of unaffiliated spacecraft.
Spacecraft orbiting more distant targets tend to always be in-beam unless in highly eccentric orbits.

## Slide 5: How Far Has the Technology Come? (1/3) The FCLTU Multiplexer (FMUX)
Mission B MOC
CLTUs
Mission A MOC
Spacecraft 1 Uplink Products
CLTUs
SLE FCLTU User
Spacecraft 2 Uplink Products
CLTUs
SLE FCLTU User
Spacecraft 3 Uplink Products
DSN Deep Space Communications Complex (DSCC)
FCLTU Multiplexer1
Uplink Processor Assembly (UPA)
Multiplexed
FCLTUs
FCLTUs
FCLTUs
Prototype FMUX developed and undergoing ground testing using DSN’s Development and Test Facility-21 (DTF-21).*
  Special thanks to the SunRISE and EscaPADE flight projects for participating in these ground tests.
    Basic FMUX functionality and project user interface demonstrated using project-supplied CLTUs.
    Proper multiplexing and reporting of radiated CLTUs demonstrated.
*Special thanks to JPL’s Multi-Mission Ground Systems & Services (MGSS) Office for sponsoring much of this development as part of the NASA SMD-funded Advanced Multi-Mission Operations System technology program.
CLTUs flow from individual MOCs to FMUX, are queued, multiplexed, and then sent to the UPA for subsequent radiation.

## Slide 6
How Far Has the Technology Come? (2/3)
The Flight Radio
What Is Needed? | What Do We Have?
Capability to switch between assigned uplink frequency and the shared MUPA session uplink frequency.1 | Iris radio has capability. Other radios do (or will) -- e.g., UST-Lite, Frontier Radio, etc.
Ability to filter out inappropriate transfer frames on basis of spacecraft ID (SCID). | Iris radio can. Most spacecraft C&DH subsystems can.
Radio capable of supporting non-standard turnaround ratios to coherently turnaround shared uplink signal frequency on individually assigned downlink frequencies. | Iris radio can now support – DTF-21 tested.2 Other radios do (or will) – e.g., UST-Lite, Frontier Radio, etc.
Radio (or C&DH in conjunction with radio) capable of compensating for perceived Doppler dynamics in single frequency uplink. | Iris radio now has a basic sweep capability + Type 3 PLL for acquisition & lock – DTF-21 tested.2 Iris radio now has FFT + Improved Carrier Tracking Loop – DTF-21 tested.2 Similar capabilities planned for UST-Lite, possibly incorporating a “Smart Sweep” algorithm.
1NASA spectrum management, in conjunction with international bodies (e.g. SFCG, ITU), may need to designate acceptable MUPA session frequencies before MUPA can be used operationally.
2Special thanks to John Baker and JPL’s Section 337 for funding the Space Dynamics Laboratory’s implementation of these capabilities.

## Slide 7: How Far Has the Technology Come? (3/3) MUPA System Engineering*
MUPA Operations Concept: Session Execution
Concept Development
Requirements Definition & Analysis
FMUX Interfaces with DSN Subsystems for In-Flight Demos & Potential Implementation
High-Level Design
*Special thanks to NASA’s Space Communications and Navigation (SCaN) Office for funding much of this work.
Work on these stages tends to be iterative.
*Other than being in-beam together, MUPA-session participants need to be using a common signaling format – part of the DSN-related MUPA user group coordination that must occur early in the session planning process.
*
*

## Slide 8: What Needs to Happen Next?
Complete prototype FMUX development and ground testing.
Complete system engineering for in-flight demonstrations.
Perform in-flight demonstrations.
FMUX
DSN Subsystem Interface Processes
FMUX
DSN Subsystem Interface Processes
Simultaneous 2-Way Doppler & Ranging.
Flight Radio
  Switchable Uplink Frequencies
  Non-standard Turnaround Ratios
  SCID Filtering
  Onboard Doppler Compensation for Acquisition & Lock
?
Implementation Funding
Perform end-to-end proof-of-concept demonstration.
FMUX
DSN Subsystem Interface Automation
Flight Radio
?
OPERATIONAL
2024
2025-2027
2028-2030