## Slide 1: Distributed architectures for cislunar communication and navigation services
Aman Chandra
Sr. Engineer for Aerospace Systems R&D

## Slide 3
Evolution of cis-lunar communications
2
South Pole Relays
Gateway
South Pole Relays
Gateway
Lunar Global Coverage
2025 - 2026
Intensive Relay service – LSP
Initial PNT service
DTE service from near side
2027 – 2030 and beyond
Intensive Relay service – LSP and far side
Lunar PNT service
Lunar Global Coverage

## Slide 4
High data-rate @ Ka-band
Low data-rate @ X-band
Low data-rate @ S band
Antenna requirements:
Multi-band and steerable antennas required
Low-power lightweight antennas for rapid deployment
Small satellite compatibility for large deployments
Cis-lunar communications – space segment

## Slide 5
Spherical Reflector Beam Steering
Spherical reflectors are symmetric about all axes
This allows efficient high-gain beam steering by moving the feed rather than the reflector or satellite, leading to significant reductions in SWAP, complexity, and cost.
Under-illuminated reflector
Lightweight feed and motors
Constant gain through wide steering angles
Customized gain through wide steering angles
Principles of Operation
Spherical reflecting surface

## Slide 6
Spherical inflatable membrane antennas
From Conception
2014 - 2017
2024
CATSAT launch in June
2022
CATSAT Delivered
2018
NASA’s CubeSat Launch Initiative for CATSAT
Space Flight Qualification Test for CATSAT
To Spaceflight
2017
FreeFall Established
Core Technology Development Funded by
NASA, NRO and US Air Force

## Slide 7
CATSAT technology development
CATSAT Flight Unit
Arecibo observatory
Line feed
1.5 U System
0.5 m spherical reflector

## Slide 8
CATSAT technology development

## Slide 9
Spherical Inflatable antenna - Lunar orbit implementation

## Slide 10
Spherical mesh reflectors
3U steerable feed system (0.7 kg)
3 U mesh reflector system (4.2 kg)
Total system mass ~ 5.5 kg
Stowed mesh reflector
Steerable feed system
1.3 m
2-meter dia parent sphere
Tape spring deployment
Back structure

## Slide 11
Spherical mesh reflectors
Deployment motor (brushless DC)
EL Motor (Piezo)
AZ motor – piezo stage
Choke horn
Septum polarizer
Split waveguide
LNA
PA
LNA and PA mounted on feed arm to reduce losses
All electronics remain inside bus
Elevation steering
Azimuth steering

## Slide 12
Modular Approach to Lunar Surface and Orbital Relay Communications
Compact deployable mesh antenna system
Spherical reflector with separate steerable feed for flexibility
Inflatable option for reduced stowed volume

## Slide 13
Lunar surface mesh telecom System
Reflector Size | 0.36 m
Frequency | 22 GHz
Steering range | 360° AZ 0-10° EL
Gain | 32.4 dB
Transmit Power | 2 W
System mass | 10.4 kg
Strawman specs
Notes:
Frequency 22 GHz for water line study, can be adjusted to standard Ka-band
EL steering for south pole site, can be increased for higher latitudes
Mass includes contingency
All components are TRL 6-9

## Slide 14
Lunar surface mesh telecom System – South pole survivability

## Slide 15
Lunar surface mesh telecom System - CONOPS

## Slide 16
THANK YOU
Dr. Aman Chandra
achandra@freefallaerospace.com
(215)479-5030
FreeFallAerospace.com
FreeFall-Aerospace